## Slide 1: MCTE 3104 Mechatronics Interfacing Lab
Session no. 4 : Serial USB – UART communication

## Slide 2: Outline
Serial Communication (USB <-> UART)
  PC <-> Arduino
  Raspi <-> Arduino
Serial Communication (Device UART <-> Device UART)
  Arduino <-> Arduino
Serial UART Arduino Software Serial Library
  Arduino <-> Bluetooth

## Slide 5
Typical device to PC interfacing
USB-UART
converter
TX
RX
GND
  When a device is connected a ‘COM’ port is established at the PC

## Slide 6
USB – UART Converter
ATMEGA16U2
CH340G
FTDI - FT232RL

## Slide 7
  You can access these established ‘COM’ port using free software such as TeraTerm, SSCOM32, etc..
Example 1: Reading values from device on PC

## Slide 8
  Since the Arduino is programmed to listen to the UART port and turns on on-board LED on when it receives ‘1’ and turns off on-board LED when it receives ‘0’.
  You can send command ‘1’ or ‘0’ using free software such as SSCOM32 or write Python script to talk to the Arduino
Example 2: Send command from PC to turn On and Off an LED attached to the Arduino

## Slide 9
Lab activity 1:
Use SSCOM tool to send commands to the Arduino that will control servo movements.
Serial Communication

## Slide 10
Typical device to Device (UART) – Device (UART) interfacing

## Slide 11
Simple device to Device (UART) – Device (UART) interfacing
Device #1
Device #2
Example 3:

## Slide 12
Simple device to Device (UART) – Device (UART) interfacing
Device #1
Device #2
Example 3: (continued)

## Slide 13
Lab activity 2:
Connect two Arduinos (using UART lines) in such a way that Arduino 1 sends movement commands in degrees and Arduino 2 listens to it and moves a servo according to the command it receives.

## Slide 14
Arduino SoftwareSerial Library
  Since the Hardware UART chip is connected to 0 and 1 which also goes to the computer via USB connection often time we want to use this port for debugging purposes by displaying on the serial monitor.
  SoftwareSerial library allows user to enable any digitial i/o pin to allow serial communication.
  You can use this to allow UART communication to other devices

## Slide 15
Arduino serial communication using softwareserial
Device #1
Device #2
Example 4:

## Slide 16
Lab activity 3:
Serial Communication
Connect two Arduinos (using UART lines) in such a way that Arduino 1 reads a potentiometer value and transmit the value via the UART lines and Arduino 2 listens to it and display values on the serial monitor.