## Slide 1: MCTE 3104 Mechatronics Interfacing Lab
Session no. 5 : Software – Hardware UART communication

## Slide 2: Outline
Software – Hardware Interfacing
  Python script to read and transmit
Device (RFID reader)
  Read RFID UID

## Slide 3: Recap
Typical device to PC interfacing
USB-UART
converter
TX
RX
GND
  When a device is connected a ‘COM’ port is established at the PC

## Slide 4
Serial communication Python to Arduino
Example 1: Reading values from Arduino
Python script
Arduino script
Serial communication Python to Arduino
Example 1: Reading values from Arduino

## Slide 5
For linux based machine, ‘COMx’ should be replace with ‘ttyx’
Serial communication Python to Arduino
Find your device by unplugging your Arduino and then plugging it back in to the raspberry pi.
type in terminal:
ls /dev/tty*

## Slide 6
Lab activity 1:
Using Arduino transmit potentiometer reading to python script running on a raspi.
Serial communication Python to Arduino

## Slide 7
Serial communication Python to Arduino
Python script
Arduino script
Example 2: Python transmitting values to Arduino

## Slide 8
Lab activity 2:
Write python script that will take angle input in degrees and transmit it to the Arduino which will then actuate a servo and move to that angle.
Serial communication Python to Arduino

## Slide 9
Interfacing our RFID reader device to PC
USB-RS232
converter
TX
RX
GND
  When a device is connected a ‘COM’ port is established at the PC

## Slide 10
Example 3: Reading RFID UID
  Use SSCOM32 to read your RFID CARD UID

## Slide 11
  Sample code that reads and verify the card read equals the hard coded UID
Example 3: Reading RFID UID

## Slide 12
Text-based data storing
Often times when you’re developing a system you’re required to save and store data. You need to store these data for further usage. Remember in the previous example we hard coded the UID to verify on the Python code itself. Imagine you have hundreds of UIDs you want to include and blacklist in your application. Hard coding the UIDs will not be a practical. One practical way is to have a separate file that stores all your UID data and have a code that reads the stored UID (data) and use them in your application.

## Slide 13
  Create a .json file called rfid-uid-database.json and then save this inside it
Example 4: Reading RFID and cross checking UID from Json file

## Slide 14
Lab activity 3:
Use the previous code to light up a green led if stored UID is read by the RFID reader and light up a red led if unknown card is read by the RFID reader.
Serial communication Python to Arduino