## Slide 1: MCTE 3104 Mechatronics Interfacing Lab
Session no. 2: Intro to Raspberry Pi

## Slide 2: Outline
Intro to Raspberry Pi
    Hardware
    OS
Raspberry Pi Pinouts
Digital I/O
  Input / Output controls
  PWM controls

## Slide 3: Technical specification of Raspberry Pi 3:
Broadcom BCM2837 64bit ARMv8 Quad Core Processor powered Single Board 1.2GHz
1GB RAM
WiFi on board
Bluetooth Low Energy (BLE) on board
40pin extended GPIO
4 x USB2 ports
Full size HDMI
CSI camera port for connecting the Raspberry Pi camera
DSI display port for connecting the Raspberry Pi touch screen display
MicroSD port for loading your operating system and storing data

## Slide 4
Raspberry PI OS
Raspberry PI Foundation provides a Raspberry PI official supported operating system called Raspbian where you can download from its official website.
Raspbian comes pre-installed with plenty of software for education, programming and general use. It has Python, Scratch, Sonic Pi, Java, Mathematica and more.
https://www.raspberrypi.org/downloads/raspbian/

## Slide 6
http://www.toptechboy.com/raspberry-pi/raspberry-pi-with-lesson-26-controlling-gpio-pins-in-python/
Picture taken from
To begin using the Raspberry Pi GPIO, we first need to know Raspi's GPIO numbering system. The two inner columns (labelled pin#) in the chart shows the ‘physical pin number’ where as the outer two columns (labelled GPIO#) of the chart shows you the ‘BCM number’ (Broadcom numbering scheme).

## Slide 7
Example 1: Writing digital output
Simple GPIO control Raspberry Pi
GPIO.setmode(GPIO.BOARD)
If you want to use physical pin convention use

## Slide 8
Lab activity 1:
Simple GPIO control Raspberry Pi
Connect 3 leds to the Raspi. Allow 1 led to blink every 0.5 second, 1 led that blinks every 1 second, and 1 that blinks every 3 seconds.

## Slide 9
PIN18
R2
Example 2: Reading digital input
Simple GPIO control Raspberry Pi
PIN17
3V3+

## Slide 10
Lab activity 2:
Simple GPIO control Raspberry Pi
Using the “Mini Strobe Siren” and linear actuator activate it with a push of a button.

## Slide 11
Example 3: PWM output on Raspberry Pi
PWM control Raspberry Pi

## Slide 12
Lab activity 3:
PWM control Raspberry Pi
Connect 2 leds to the Raspberry Pi and create a different fading effect to individual leds.